## Slide 1
Mud Interlocking Brick
The honest comparison — pros, cons & real cost savings
Compressed Stabilised Earth Block (CSEB) · evidence-based · sources cited
TERRABLOCK · TELANGANA

## Slide 2
THE BIG PICTURE
Should you build with mud interlocking brick?
The honest answer: yes — for the right building, in the right climate. Here is the evidence.
15–35%
lower wall cost vs conventional brick
−80%
laying labour (no mortar, dry-stack)
11–13×
less energy & CO₂ than fired clay
But it is not magic. It has real limits — water, height, curing time. We cover those too.
Sources: Auroville Earth Institute; Brick&Bolt; IIT Kanpur NICEE; CivilTutorials. Full citations on final slide.
02

## Slide 3
WHAT IT IS
Soil, a little cement, and a clever shape
Local soil + 5–8% cement
Sieved soil mixed with a little cement and water — no firing, no kiln.
Pressed, not burnt
Compressed in a hydraulic press, then cured for ~28 days to full strength.
Interlocking shape
Tongue-and-groove edges lock together — stacked dry, with little or no mortar.
Source: Auroville Earth Institute (earth-auroville.com); IIT Kanpur NICEE. Governed in India by BIS IS 1725.
03

## Slide 4
THE PROS
Six real advantages
Cheaper walls
15–35% lower wall cost than fired brick
Faster build
Mortarless stacking cuts laying time 20–30%
No plaster, no paint
Smooth exposed faces — skip plaster & paint
Cooler inside
Earth walls stay cooler — ideal for hot Telangana
Low carbon
11–13× less energy & CO₂ than fired clay
Quake-friendly
Reinforced interlocking walls flex, don't shatter
Sources: Brick&Bolt; CivilTutorials; Auroville Earth Institute; IIT Kanpur NICEE (seismic).
04

## Slide 5
COST SAVINGS
Where the money is saved
No external plaster
25–35% of wall cost — exposed finish
Little/no mortar
20% saved on mortar & plaster materials
Dry-stack labour
up to 80% less laying labour
Build time
20–30% faster construction
Net result: a finished CSEB wall runs 15–20% cheaper than fired brick (up to ~40% in some studies).
Sources: Brick&Bolt (plaster −25–35%); CivilTutorials (mortar −20%, time −20–30%); IIT Kanpur (labour −80%); Auroville/Happho (15–40% cheaper).
05

## Slide 6
REALITY CHECK
“Can we build a house in 1 week?”
The myth
“Just stack the blocks — a whole house goes up in 7 days, start to finish.”
Not the whole house. Foundation, roof, plumbing and wiring still take their normal time.
The fact
Walls go up in days.
Mortarless stacking cuts laying labour ~80% and time 20–30%.
BUT the blocks must cure ~28 days first
— done at the factory, so pre-cured blocks let the site shell finish in about a week.
Sources: IIT Kanpur NICEE (labour −80%); CivilTutorials (time −20–30%); Auroville Earth Institute (28-day curing).
06

## Slide 7
REALITY CHECK
“No plastering and no painting?”
Mostly TRUE
Plaster is optional, inside and out.
Smooth faces = exposed-brick look (a design trend). Saves 25–35% of wall cost. No mortar means no plaster base — and the natural earth tone needs no paint.
The caveats
Fill the joints — gaps invite ants/insects.
Seal exposed faces in heavy rain — earth blocks lose 40–60% strength when soaked.
Good news: semi-arid Telangana is a strong fit for exposed finish.
Sources: Brick&Bolt (plaster optional, −25–35%, rain caveat); NCBI/PMC (saturated strength loss 42–62%).
07

## Slide 8
THE GREEN EDGE
The lowest-carbon brick you can buy
11×
less energy to make than a fired-clay brick
13×
less CO₂ pollution than a fired-clay brick
~95%
local soil — barely any transport or mining
No kiln means no coal, no fired-brick smoke — the single biggest pollution source in Indian brick-making.
Sources: Auroville Earth Institute (11× energy, 13× CO₂); IIT Kanpur NICEE (1/5–1/15 manufacturing energy).
08

## Slide 9
THE CONS
The honest limitations
Weak when wet
Loses 40–60% strength soaked — needs sealing & good roof overhangs
Low-rise only
Lower strength than concrete block — best for G+1 / G+2 homes
28-day cure
Blocks must cure ~4 weeks before use — plan factory stock ahead
Soil-dependent
Needs the right soil; cement % (5–10%) tuned to each soil
Perception
“Mud = poor” stigma — needs education & show-homes to sell
Quality control
Strength varies with press & curing discipline — BIS IS 1725 testing a must
Sources: NCBI/PMC (saturated strength); IIT Kanpur (strength vs concrete); Auroville & block-machine.net (28-day cure); ScienceDirect (soil/cement).
09

## Slide 10
HEAD TO HEAD
Mud interlocking vs the alternatives
 | Mud Interlocking | Fired Clay | Fly Ash
Price / unit | ₹25–52 / block | ₹8–12 / brick | ₹5–8 / brick
Mortar | Little / none | Required | Required
Plaster + paint | Optional (skip it) | Required | Required
Laying speed | Fast — dry stack | Slow | Slow
Strength (MPa) | 3–7.8 | 3–10 | 3–10
Energy / CO₂ | Very low | High (kiln) | Medium
Water resistance | Needs sealing | Good | Good
Best for | Low-rise, dry, green | All-round | Bulk / cheap
Sources: CivilTutorials & IndiaMart (price); IIT Kanpur & block-machine.net (strength); Auroville (energy); Brick&Bolt (finish).
10

## Slide 11
THE VERDICT
When to use it — and when not to
Use it for
Low-rise homes (G+1, G+2)
Hot, dry climates — like Telangana
Exposed / natural-finish design
Green-rated & cost-led projects
Sites with good local soil
Think twice for
High-rise / heavy load buildings
Flood-prone or very wet regions
Unprotected walls with no roof overhang
Sites with poor or sandy-only soil
Buyers who reject the look
Telangana is semi-arid and low-rise-dominated — a strong natural fit for mud interlocking brick.
11

## Slide 12
SOURCES
Every claim, traceable
Auroville Earth Institute — earth-auroville.com
Cost 15–20% lower; 11× energy, 13× CO₂; 28-day curing
IIT Kanpur — NICEE (WCEE 2012) — iitk.ac.in/nicee
Labour −80%; strength 7.76 MPa; 1/5–1/15 energy; seismic
Brick&Bolt — bricknbolt.com
Plaster optional, wall −25–35%; exposed finish; rain caveat
CivilTutorials — civiltutorials.com
Price ₹25–40/block; time −20–30%; mortar/plaster −20%
NCBI / PMC — ncbi.nlm.nih.gov
Saturated strength loss 42–62%; 10% cement → 5.92 MPa
Happho / Frontiers — happho.com
Up to ~40% cheaper; 13% cheaper than RCC+brick apartment
IndiaMart (market price) — indiamart.com
CSEB 300×150×90 mm ₹30/unit; interlocking ₹52/piece
BIS IS 1725 — bis.gov.in
Indian standard for stabilised soil blocks
Research compiled June 2026 · figures are indicative ranges from public sources, not adversarially verified.